INSTRUCTIONS

On 15 December 2020, BCA issued a circular to inform the industry of the changes related to the Temporary Occupation Permit (TOP)/ Certificate of Statutory Completion (CSC) application requirements for landed house built for the owner’s own use including new erection, re-construction and A&A works.

The QP for the building works for landed house built for owner’s own use no longer need to book a TOP inspection. When the project is ready for application of TOP/CSC, the QP shall submit his/her inspection report/checklist as part of the supporting documents for the application of TOP/CSC. QP can submit the TOP/CSC application via e-CORENET directly, instead of via the TOP Portal.

As part of our continuous efforts to improve the current processes, we have made some changes to the previous checklist.

The QP for the building works shall use this document to prepare his/her inspection report/checklist as part of the supporting documents for the application of TOP/CSC.

The Professional Engineer (Electrical) for the lightning protection system shall prepare his separate report (e.g. Certificate of Supervision of Lightning Protection System, As-built Plans, Test Reports, Site Inspection Report) and provide to the QP for building works as part of the overall TOP/CSC submission. See Appendix B as a guide.

The Professional Engineer (Mechanical) shall provide the Certificate of Supervision of Air-conditioning/Mechanical Ventilation System for any ACMV installation indicated on the building plans.

The owner of lift shall apply for PTO via the Online Permit to Operate (OPTO) system.  As a continuing effort in providing better service to the industry with a more intuitive user experience, the new Lifts and Escalators Application (“LEAP”) Portal portal (https://www2.bca.gov.sg/LEAP), which will replace the existing Online Permit To Operate (“OPTO”) system, will go live on 21 November 2022 0900 hrs.

We have prepared three appendices for guidance.

- Appendix A: Guideline and sample of Site Inspection Report for Residential Landed House (Built for The Owner’s Own Use)

- Appendix B: Guideline for Supervising PE (Electrical) to provide photographs for lightning protection system, in lieu of physical site inspection

- Appendix C: Supporting documents for the application of TOP/CSC

This document is for QP’s use

PROJECT INFORMATION

| 1 | Project Reference No. |  |
| --- | --- | --- |
| 2 | Project Title |  |

CLAUSES IN APPROVED DOCUMENT

The QP shall indicate the clauses that are applicable for the building works and the status of compliance. For clauses that obtained waiver approval (or owner’s undertaking), QP may indicate under remarks column. The QP may also provide further information (e.g. material specifications) if deemed necessary.

| S/N | Clauses in the Approved Document | Status of compliance (Yes/No/Not applicable) | Remarks, if any |
| --- | --- | --- | --- |
| 1 | C - Headroom and Ceiling Height |  |  |
| 2 | E - Staircases |  |  |
| 3 | F -Lighting |  |  |
| 4 | G - Ventilation |  |  |
| 5 | H - Safety from Falling |  |  |
| 6 | J - Roof |  |  |
| 7 | K - Lift and Escalators |  |  |
| 8 | L - Lightning Protection |  |  |
| 9 | M - Safety of Windows |  |  |
| 10 | N - Use of Glass at Height |  |  |
| 11 | P -Daylight Reflectance |  |  |

This document is for QP’s use

SITE INSPECTION REPORT

- Under Section 9 of the Building Control Act, the QP is required to ensure that the building works comply with the regulatory requirements

- The submission of site inspection report is in lieu of the physical joint TOP inspection.

- The QP shall compile the photos/measurements for the items listed in Sections 1 and 2 below.

- QP is required to annotate the locations of photos on site/floor plan clearly. The QP shall refer to Appendix A as a guide to complete Sections 1 and 2 below.

| SECTION 1A: GENERAL OVERVIEW OF COMPLETED BUILDING AND SECTION 1B: GENERAL LAYOUT OF ALL FLOORS TO SHOW COMPLETION (BASEMENT TO ATTIC) |
| --- |
| Front Elevation | Rear elevation | Side elevation |
| Basement | 1st Storey | 2nd Storey |
| 3rd storey | Attic | Mezzanine (If applicable) |

| SECTION 2: COMPLIANCE OF CLAUSES |
| --- |
| Clauses in Approved Document | Photographs/ Location/Measurements | Remark (if any) |
| Headroom and Ceiling Height |  |  |
| Staircases |  |  |
| Safety From Falling |  |  |

QP can insert more rows and insert photos. See Appendix A as a guide

I certify that the site has been inspected and complies with the requirements of the Building Control Act and Regulation, and the relevant Singapore Standard Code of Practice.

Submitted by:

__________________________________                                       	                ______________

Name and Signature of QP 	Date